## Slide 1: Extendible roof platforms for busses
Presentation of Pfaffs’ extendable roof platforms for buses

## Slide 2: Dendro Lift AB
Swedish company with own development and manufacturing in Järvsö Scandinavian agent for German Pfaff Silberblau for extendible roof platforms and train lifts Focused on lifting heavy vehicles, industrial lifting solutions and safe working at heights Nearly 50 years of heavy lifting experience Customized solutions based on standard components Works according to ISO 9001:2008 and ISO 14001:2004

## Slide 3: New buses with equipment on the roof

## Slide 4: Example of roof equipment on an electric bus

## Slide 5: Work at height
One of the most common and serious types of workplace accidents is work at height Fixed fall protection better than personal
The Swedish Work Environment Authority (Arbetsmiljöverket) states:
“Personal protective equipment can only be used in exceptional cases where collective protection is not possible to use, or where the time to get these devices in place takes significantly longer than it takes to carry out the work task in question.”

## Slide 6: Safe work on the roof of the vehicle
Extendible roof platforms are common within the railway industry where the trains have had lots of components on the roof for a long time.
The same technology works for busses
Pfaff and Dendro Lift has a lot of experience from large installations around the world

## Slide 7: Roof platform for busses
Available with both fixed and flexible height
  Can be combined with a sub-floor or wheel lift
The fixed height can be customized according to needs
Flexible height 1,0 - 4,4 m
The lenght ca be customized according to needs: 12, 15, 18, 21 or 24 m
Can be placed in a row
Can be customized to existing buildings
The staircase is automatically adjusted to the height

## Slide 8: Roof platforms for busses
Example

## Slide 9: Roof platform with adjustable height
If flexible height is chosen, the platforms can be adjusted to the vehicle's roof height as well as being lowered, which is useful for example when changing windows.

## Slide 10: The possibility to change side windows
By lowering the platform, it can be used to, as an example, change windows or other work on the side of the bus.

## Slide 11: Working platform
Length of segment = 6 - 10 m Other measurements are available
Length when extended = 500 mm 200-800 mm possible
Width of fixed platform = 755 mm

## Slide 12: Example drawing

## Slide 13: Working platform
Creates a smooth floor against the vehicle
Non-slip protection according to class R11/R12
Risk of falling is eliminated

## Slide 14: Automatic stop
On all segments there is a soft safety edge protection that automatically stops the platform when it meets the vehicle, then reverse it back about 5 mm. As an option, the solution can be supplemented with ultrasonic transducers that stop the platforms just before contact with the vehicle. These work regardless of the material (metal, plastic, glass, etc.) that it goes against.

## Slide 15: Height-Adjustable Platforms
Ability to automatically raise both platforms in order to fit buses with different ceiling heights Lifting speed approx. 500mm/min Lifting mechanism on the pillars, based on self-locking trapezoid threaded screw jacks Powered by synchronized 3-Phase brake motors Staircase that automatically adapts to the new height

## Slide 16: Adjustable staircase with correct step height

## Slide 17: Door to stair case
The door is monitored and locked if the platforms are not extended to the bus.
The door closes automatically by spring loaded adjustable hinges.

## Slide 18: Control cabinet
Desing can be customized accoring to needs.
Is mounted under the fixed platform, under the staircase or on a placement of your choosing in connection to the roof platform.

## Slide 19: Operator panel
  The operator panel i placed on the central control cabinet. Here you choose how the platforms are used via a touch display.
  If the platforms are height adjustable, it is done here.
  Remote control with a long cord gives an overbiew when adjusting height and width

## Slide 20: Control panel
Touch display in English or local language to control all or individual platform segments. Individual segments can be retracted separately.

## Slide 21: Kontrollpanel
Touch display in English or local language to control all or individual platform segments.
All lifts are driven synchronized.
  Possible to have a slight height difference between right and left side in order to handle different bus models.
All platforms can be extended synchronized and individual segments can be withdrawn separately

## Slide 22: Platform installation
Comes complete, including stairs, guardrails, pillars to the floor 4 pillars per side, in the center under each platform Affixed with Chemical anchor bolts
Installation time approx. 1 week

## Slide 23: Platform control
One 0.11 kW AC motor of per segment. Rack and pinion operation. Sliding platform extension 200-600 mm (can be up to 800 mm).
  200-400 mm recommended

## Slide 24: Safety gates at the end
Aluminum swivel gate. Electronically supervised. Adjustable longitudinal, with crank or electrically

## Slide 25: Removable front bridge
For maintenance at the front of the vehicle (front window etc.) there is a removable front bridge, that can be laid on the front-end sides of the platforms by an over head crane

## Slide 26: Guardrails
110 cm high guard rails with kick plate and safety net.

## Slide 27: Traffic lights at the end
Green light shows that the platforms are contracted and that it’s free to drive bus in or out.
If the platforms have adjustable height, each pillar is equipped with at blinking light to indicate movement

## Slide 28: Lamps under the platforms
Built in LED lamps under the platforms provides good working light underneath

## Slide 29: Other
Max 5 people on the platform at the same time
Can be delivered in any RAL color.
CE marked according to ISO 14122 (requirements for safe access to machinery) and Machinery Directive 2006/42 EC.
Requires 40A fuse for adjustable height, 10A for fixed
Shipping, installation, training and documentation is included.
Installation time is about 1-2 weeks.
Delivery time about 4-6 months
Swedish references:
  Brixly Jönköping
  Skellefteå Bus
  Jernhusen, Sävenäs, Gothenburg
  Mälab, Eskilstuna
  BS Verkstäder, Falköping